3D Grapher parametric equations for de Broglie wave generation from charged photon – Richard Gauthier richgauthier@gmail.com

3D Grapher program for PC’s can be obtained at romanlab.com/3dg

velocity of electron is set at 0.5c by the v variable (can be varied)

PLOT OPTIONS

Intervals:

Min X   -20       Max X   100       Line and dot colors and sizes have to be selected separately

Min Y   -20       Max Y   100

Min Z   -20        Max Z   100

Animation:

Min t      Max t     Steps

0               11           50

Mode: Repeat    Frames/sec: 10

Line 1	Photon helix 			              	       Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*u*v

y(u,v,t)= (1*(1-v^2) ) * sin(1*(u)/((1-v^2)^.5 ) )		0	200	400	0.5      0.5	0

z(u,v,t)= (1*(1-v^2) ) * cos(1*(u)/((1-v^2)^.5) )

Line 2	Photon dot on helix		                  	       Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*t*v

y(u,v,t)= (1*(1-v^2) ) *sin(1*(t)/((1-v^2)^.5 ) )  		0	6.28	100	0.5      0.5     0

z(u,v,t)= (1*(1-v^2) ) * cos(1*(t)/((1-v^2)^.5 ) )

Line 3	electron red trajectory			                 Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*u*v

y(u,v,t)= 0							0	200	50	0.5     0.5     0

z(u,v,t)=0

Line 4	electron red dot			                Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*t*v

y(u,v,t)= 0						      -25           25       50        	0.5     0.5     0

z(u,v,t)=0

Line 5	unrolled helix line			                 Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*u*v

y(u,v,t)= u*(1-v^2)^.5						0	50	50	0.5     0.5     0

z(u,v,t)=0

Line 6	blue point on unrolled helix line		      Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1* (t) *v

y(u,v,t)= (t)*(1-v^2)^.5				        -25	25	50	0.5     0.5     0

z(u,v,t)=0

Line 7	lowest wavefront line				      Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*(t) *v  +    u*(1-v^2)^.5

y(u,v,t)= (t)*(1-v^2)^.5    -   1*(u)*v  		        0	          100       50        0.5     0.5       0

z(u,v,t)=0

Line 8	second wavefront line				      Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*(t+11)*v  +    u*(1-v^2)^.5

y(u,v,t)= (t+11)*(1-v^2)^.5    -   1*(u)*v  		        0		100	50	0.5     0.5        0

z(u,v,t)=0

Line 9	third wavefront line			                  Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*(t+22)*v  +    u*(1-v^2)^.5

y(u,v,t)= (t+22)*(1-v^2)^.5    -   1*(u)*v  		        0	         100     50         0.5    0.5      0

z(u,v,t)=0

Line 10  fourth wave front line			    Min u     Max u  Steps    Min v Max v  Steps

x(u,v,t)= 1*(t+33)*v  +    u*(1-v^2)^.5

y(u,v,t)= (t+33)*(1-v^2)^.5    -   1*(u)*v  		        0	       100     50              0.5    0.5      0

z(u,v,t)=0